## Slide 1
IT5002
Computer Systems and Applications
Number Systems
colintan@nus.edu.sg

## Slide 2: Q & A
DO NOT use the Zoom chat for questions. It doesn’t appear in the video recordings.
Please ask questions at https://sets.netlify.app/module/61597486a7805d9fb1b4accd
OR scan this QR code (may be obscured on some slides)

## Slide 3: Lecture 3: Number Systems
Data Representation
Decimal (base 10) Number System
Other Number Systems
Base-R to Decimal Conversion
Decimal to Binary Conversion
  5.1 Repeated Division-by-2
  5.2 Repeated Multiplication-by-2
Conversion Between Decimal and Other Bases
Conversion Between Bases
Binary to Octal/Hexadecimal Conversion

## Slide 4: Lecture 3: Number Systems
ASCII Code
Negative Numbers
  10.1 Sign-and-Magnitude
  10.2 1s Complement
  10.3 2s Complement
  10.4 Comparisons
  10.5 Complement on Fractions
  10.6 2s Complement Addition/Subtraction
  10.7 1s Complement Addition/Subtraction
  10.8 Excess Representation
Real Numbers
  11.1 Fixed-Point Representation
  11.2 Floating-Point Representation

## Slide 5: 1. Data Representation
5
Basic data types in C:
int
float
double
char
Variants: short, long
How data is represented depends on its type:
01000110
As an ‘int’, it is 70
As a ‘char’, it is ‘F’
11000000110100000000000000000000
As an ‘int’, it is -1060110336
As an ‘float’, it is -6.5

## Slide 6: 1. Data Representation
Data are internally represented as sequence of bits (binary digits). A bit is either 0 or 1.
Other units
  Byte: 8 bits
  Nibble: 4 bits (rarely used now)
  Word: Multiple of bytes (eg: 1 byte, 2 bytes, 4 bytes, etc.) depending on the computer architecture
N bits can represent up to 2N values
  Eg: 2 bits represent up to 4 values (00, 01, 10, 11); 4 bits represent up to 16 values (0000, 0001, 0010, …., 1111)
To represent M values, log2M bits required
  Eg: 32 values require 5 bits; 1000 values require 10 bits

## Slide 7: 2. Base 10 Number System
A weighted-positional number system.
Base (also called radix) is 10
Symbols/digits = { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Each position has a weight of power of 10
  Eg: (7594.36)10 = (7 × 103) + (5 × 102) + (9 × 101) + (4 × 100) + (3 × 10-1) + (6 × 10-2)
(anan-1… a0 . f1f2 … fm)10 = (an x 10n) + (an-1x10n-1) + … + (a0 x 100) + (f1 x 10-1) + (f2 x 10-2) + … + (fm x 10-m)

## Slide 8: 3. Other Number Systems
A weighted-positional number system.
Base (also called radix) is 10
Symbols/digits = { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Each position has a weight of power of 10
  Eg: (7594.36)10 = (7 × 103) + (5 × 102) + (9 × 101) + (4 × 100) + (3 × 10-1) + (6 × 10-2)
(anan-1… a0 . f1f2 … fm)10 = (an x 10n) + (an-1x10n-1) + … + (a0 x 100) + (f1 x 10-1) + (f2 x 10-2) + … + (fm x 10-m)

## Slide 9: 3. Other Number Systems
In some programming languages/software, special notations are used to represent numbers in certain bases
  In programming language C
    Prefix 0 for octal. Eg: 032 represents the octal number (32)8
    Prefix 0x for hexadecimal. Eg: 0x32 represents the hexadecimal number (32)16
  In QTSpim (a MIPS simulator you will use)
    Prefix 0x for hexadecimal. Eg: 0x100 represents the hexadecimal number (100)16
  In Verilog, the following values are the same
    8’b11110000: an 8-bit binary value 11110000
    8’hF0: an 8-bit binary value represented in hexadecimal F0
    8’d240: an 8-bit binary value represented in decimal 240

## Slide 10: 4. Base-R to Decimal Conversion
Easy!
  1101.1012 = 123 + 122 + 120 + 12-1 + 12-3
= 8 + 4 + 1 + 0.5 + 0.125 = 13.62510
  572.68 =
  2A.816 =
582 + 781 + 280 + 68-1
= 320 + 56 + 2 + 0.75 = 378.7510
  341.245 =
2161 + 10160 + 816-1
= 32 + 10 + 0.5 = 42.510
352 + 451 + 150 + 25-1 + 45-2
= 75 + 20 + 1 + 0.4 + 0.16 = 96.5610


## Slide 11: 5. Decimal to Binary (Base-2) Conversion
For whole numbers
  Repeated Division-by-2 Method
For fractions
  Repeated Multiplication-by-2 Method

## Slide 12: 5.1 Decimal to Binary (Base-2) Conversion: Repeated Divide
To convert a whole number to binary, use successive division by 2 until the quotient is 0. The remainders form the answer, with the first remainder as the least significant bit (LSB) and the last as the most significant bit (MSB).
(43)10 = ( ? )2

## Slide 13: 5.1 Decimal to Binary (Base-2) Conversion: Repeated Divide
To convert a whole number to binary, use successive division by 2 until the quotient is 0. The remainders form the answer, with the first remainder as the least significant bit (LSB) and the last as the most significant bit (MSB).
(43)10 = ( ? )2
101011

## Slide 14: 5.2 Decimal to Binary (Base-2) Conversion: Repeated Multiply
To convert decimal fractions to binary, repeated multiplication by 2 is used, until the fractional product is 0 (or until the desired number of decimal places). The carried digits, or carries, produce the answer, with the first carry as the MSB, and the last as the LSB.
(0.3125)10 = ( ? )2

## Slide 15: 5.2 Decimal to Binary (Base-2) Conversion: Repeated Multiply
To convert decimal fractions to binary, repeated multiplication by 2 is used, until the fractional product is 0 (or until the desired number of decimal places). The carried digits, or carries, produce the answer, with the first carry as the MSB, and the last as the LSB.
(0.3125)10 = ( ? )2
.0101

## Slide 16: 6. Conversion from Decimal to Other Bases
Base-R to decimal: multiply digits with their corresponding weights
Decimal to binary (base 2)
  Whole numbers: repeated division-by-2
  Fractions: repeated multiplication-by-2
Decimal to base-R
  Whole numbers: repeated division-by-R
  Fractions: repeated multiplication-by-R

## Slide 17: 7. Conversion Between Bases
In general, conversion between bases can be done via decimal:
Shortcuts for conversion between bases 2, 4, 8, 16 (see next slide)
Base-2 Base-2
Base-3 Base-3
Base-4 Decimal Base-4
… ….
Base-R Base-R

## Slide 18: 8. Binary to Octal / Hexadecimal Conversion
Binary  Octal: partition in groups of 3
  (10 111 011 001 . 101 110)2 =
Octal  Binary: reverse
  (2731.56)8 =
Binary  Hexadecimal: partition in groups of 4
  (101 1101 1001 . 1011 1000)2 =
Hexadecimal  Binary: reverse
  (5D9.B8)16 =

(2731.56)8
(10 111 011 001 . 101 110)2
(5D9.B8)16
(101 1101 1001 . 1011 1000)2

## Slide 20: 9. ASCII Code
ASCII code and Unicode are used to represent characters (‘a’, ‘C’, ‘?’, ‘\0’, etc.)
ASCII
  American Standard Code for Information Interchange
  7 bits, plus 1 parity bit (odd or even parity)

## Slide 21: 9. ASCII Code
ASCII table
‘A’: 1000001 (or 6510)

## Slide 22: 9. ASCII Code
Integers (0 to 127) and characters are ‘somewhat’ interchangeable in C
int num = 65;
char ch = 'F';
printf("num (in %%d) = %d\n", num);
printf("num (in %%c) = %c\n", num);
printf("\n");
printf("ch (in %%c) = %c\n", ch);
printf("ch (in %%d) = %d\n", ch);
CharAndInt.c
num (in %d) = 65
num (in %c) = A
ch (in %c) = F
ch (in %d) = 70

01000110
As an ‘int’, it is 70
As a ‘char’, it is ‘F’

## Slide 24: PAST YEAR QUESTION
int i, n = 2147483640;
for (i=1; i<=10; i++) {
n = n + 1;
}
printf("n = %d\n", n);
PastYearQn.c
What is the output of the above code when run on sunfire?
Is it 2147483650?

## Slide 25: 10. Negative Numbers
Unsigned numbers: only non-negative values
Signed numbers: include all values (positive and negative)
There are 3 common representations for signed binary numbers:
  Sign-and-Magnitude
  1s Complement
  2s Complement

## Slide 26: 10.1 Negative Numbers: Sign and Magnitude
The sign is represented by a ‘sign bit’
  0 for +
  1 for -
Eg: a 1-bit sign and 7-bit magnitude format.
sign
magnitude
  00110100  +1101002 = +5210
  10010011  -100112 = -1910

## Slide 27: 10.1 Negative Numbers: Sign and Magnitude
Largest value: 01111111 = +12710
Smallest value: 11111111 = -12710
Zeros: 00000000 = +010 10000000 = -010
Range (for 8-bit): -12710 to +12710
Question:
  For an n-bit sign-and-magnitude representation, what is the range of values that can be represented?

## Slide 28: 10.1 Negative Numbers: Sign and Magnitude
To negate a number, just invert the sign bit.
Examples:
  How to negate 00100001sm (decimal 33)? Answer: 10100001sm (decimal -33)
  How to negate 10000101sm (decimal -5)? Answer: 00000101sm (decimal +5)

## Slide 29: 10.2 Negative Numbers: 1’s Complement
Given a number x which can be expressed as an n-bit binary number, its negated value can be obtained in 1s-complement representation using:
-x = 2n – x – 1
Example: With an 8-bit number 00001100 (or 1210), its negated value expressed in 1s-complement is:
-000011002 = 28 – 12 – 1 (calculation done in decimal) = 243 = 111100111s
(This means that -1210 is written as 11110011 in 1s-complement representation.)

## Slide 30: 10.2 Negative Numbers: 1’s Complement
Technique to negate a value: invert all the bits.
Largest value: 01111111 = +12710
Smallest value: 10000000 = -12710
Zeros: 00000000 = +010 11111111 = -010
Range (for 8 bits): -12710 to +12710
Range (for n bits): -(2n-1 – 1) to 2n-1 – 1
The most significant bit (MSB) still represents the sign: 0 for positive, 1 for negative.

## Slide 31: 10.2 Negative Numbers: 1’s Complement
Examples (assuming 8-bit):
(14)10 = (00001110)2 = (00001110)1s
-(14)10 = -(00001110)2 = (11110001)1s
-(80)10 = -( ? )2 = ( ? )1s

## Slide 32: 10.3 Negative Numbers: 2’s Complement
Given a number x which can be expressed as an n-bit binary number, its negated value can be obtained in 2s-complement representation using:
-x = 2n – x
Example: With an 8-bit number 00001100 (or 1210), its negated value expressed in 2s-complement is:
-000011002 = 28 – 12 (calculation done in decimal) = 244 = 111101002s
(This means that -1210 is written as 11110100 in 2s-complement representation.)

## Slide 33: 10.3 Negative Numbers: 2’s Complement
Technique to negate a value: invert all the bits, then add 1.
Largest value: 01111111 = +12710
Smallest value: 10000000 = -12810
Zero: 00000000 = +010
Range (for 8 bits): -12810 to +12710
Range (for n bits): -2n-1 to 2n-1 – 1
The most significant bit (MSB) still represents the sign: 0 for positive, 1 for negative.

## Slide 34: 10.3 Negative Numbers: 2’s Complement
Examples (assuming 8-bit):
(14)10 = (00001110)2 = (00001110)2s
-(14)10 = -(00001110)2 = (11110010)2s
-(80)10 = -( ? )2 = ( ? )2s
Compare with slide 29.
1s complement:
(14)10 = (00001110)2 = (00001110)1s
-(14)10 = -(00001110)2 = (11110001)1s

## Slide 35: 10.4 Negative Numbers: Comparison
4-bit system
Positive values Negative values
Value | Sign-and-Magnitude | 1s Comp. | 2s Comp.
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
+0 | 0000 | 0000 | 0000
Value | Sign-and-Magnitude | 1s Comp. | 2s Comp.
-0 | 1000 | 1111 | -
-1 | 1001 | 1110 | 1111
-2 | 1010 | 1101 | 1110
-3 | 1011 | 1100 | 1101
-4 | 1100 | 1011 | 1100
-5 | 1101 | 1010 | 1011
-6 | 1110 | 1001 | 1010
-7 | 1111 | 1000 | 1001
-8 | - | - | 1000

## Slide 36
Past-Year’s Exam Question! (Answer)

int i, n = 2147483640;
for (i=1; i<=10; i++) {
n = n + 1;
}
printf("n = %d\n", n);
PastYearQn.c
What is the output of the above code when run on sunfire?
Is it 2147483650?
int type in sunfire takes up 4 bytes (32 bits) and uses 2s complement
Largest positive integer = 231 – 1 = 2147483647
1st iteration: n = 2147483641
7th iteration: n = 2147483647
01111 ……. 1111111111
8th iteration: n = -2147483648
10000…….0000000000
+ 1
9th iteration: n = -2147483647
10th iteration: n = -2147483646


## Slide 37: 10.5 Negative Numbers: Complements on Fractions
We can extend the idea of complement on fractions.
Examples:
  Negate 0101.01 in 1s-complement Answer: 1010.10
  Negate 111000.101 in 1s-complement Answer: 000111.010
  Negate 0101.01 in 2s-complement Answer: 1010.11

## Slide 38: 10.6 Negative Numbers: 2’s Complements on Additions and Subtractions
Algorithm for addition of integers, A + B:
  Perform binary addition on the two numbers.
  Ignore the carry out of the MSB.
  Check for overflow. Overflow occurs if the ‘carry in’ and ‘carry out’ of the MSB are different, or if result is opposite sign of A and B.
Algorithm for subtraction of integers, A – B: A – B = A + (-B)
  Take 2s-complement of B.
  Add the 2s-complement of B to A.

## Slide 39: 10.6 Negative Numbers: Overflow
Signed numbers are of a fixed range.
If the result of addition/subtraction goes beyond this range, an overflow occurs.
Overflow can be easily detected:
  positive add positive  negative
  negative add negative  positive
Example: 4-bit 2s-complement system
  Range of value: -810 to 710
  01012s + 01102s = 10112s 510 + 610 = -510 ?! (overflow!)
  10012s + 11012s = 101102s (discard end-carry) = 01102s -710 + -310 = 610 ?! (overflow!)

## Slide 40: 10.6 Negative Numbers: Overflow
Examples: 4-bit system
Which of the above is/are overflow(s)?
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
-2 1110
+ -6 + 1010
---- -------
-8 11000
---- -------
+6 0110
+ -3 + 1101
---- -------
+3 10011
---- -------
+4 0100
+ -7 + 1001
---- -------
-3 1101
---- -------
No overflow
-3 1101
+ -6 + 1010
---- -------
-9 10111
---- -------
+5 0101
+ +6 + 0110
---- -------
+11 1011
---- -------
No overflow
Overflow!
Overflow!
No overflow
No overflow

## Slide 41: 10.6 Negative Numbers: Overflow
Examples: 4-bit system
  4 – 7
  Convert it to 4 + (-7)
+4 0100
+ -7 + 1001
---- -------
-3 1101
---- -------
Which of the above is/are overflow(s)?
  6 – 1
  Convert it to 6 + (-1)
+6 0110
+ -1 + 1111
---- -------
+5 10101
---- -------
  -5 – 4
  Convert it to -5 + (-4)
-5 1011
+ -4 + 1100
---- -------
-9 10111
---- -------
No overflow
No overflow
Overflow!

## Slide 42: 10.7 Negative Numbers: 1’s Complement on Additions and Subtractions.
Algorithm for addition of integers, A + B:
  Perform binary addition on the two numbers.
  If there is a carry out of the MSB, add 1 to the result.
  Check for overflow. Overflow occurs if result is opposite sign of A and B.
Algorithm for subtraction of integers, A – B: A – B = A + (-B)
  Take 1s-complement of B.
  Add the 1s-complement of B to A.

## Slide 43: 10.7 Negative Numbers: 1’s Complement Addition
Examples: 4-bit system
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
+5 0101
+ -5 + 1010
---- -------
-0 1111
---- -------
-2 1101
+ -5 + 1010
---- -------
-7 10111
---- + 1
-------
1000
-------
-3 1100
+ -7 + 1000
---- -------
-10 10100
---- + 1
-------
0101
-------
Any overflow?
No overflow
No overflow
No overflow
Overflow!
DLD page 42 – 43 Quick Review Questions Questions 2-13 to 2-18.

## Slide 44: 10.8 Negative Numbers: Excess Notation
Besides sign-and-magnitude and complement schemes, the excess representation is another scheme.
It allows the range of values to be distributed evenly between the positive and negative values, by a simple translation (addition/subtraction).
Example: Excess-4 representation on 3-bit numbers. See table on the right.
Excess-4 Representation | Value
000 | -4
001 | -3
010 | -2
011 | -1
100 | 0
101 | 1
110 | 2
111 | 3
Questions: What if we use Excess-2 on 3-bit numbers? Or Excess-7?

## Slide 45: 10.8 Negative Numbers: Excess Notation
Example: For 4-bit numbers, we may use excess-7 or excess-8. Excess-8 is shown below.
Excess-8 Representation | Value
0000 | -8
0001 | -7
0010 | -6
0011 | -5
0100 | -4
0101 | -3
0110 | -2
0111 | -1
Excess-8 Representation | Value
1000 | 0
1001 | 1
1010 | 2
1011 | 3
1100 | 4
1101 | 5
1110 | 6
1111 | 7

## Slide 46: 11 Real Numbers
Many applications involve computations not only on integers but also on real numbers.
How are real numbers represented in a computer system?
Due to the finite number of bits, real number are often represented in their approximate values.

## Slide 47: 11.1 Real Numbers Fixed Point Representation
In fixed-point representation, the number of bits allocated for the whole number part and fractional part are fixed.
For example, given an 8-bit representation, 6 bits are for whole number part and 2 bits for fractional parts.
assumed binary point
integer part
fraction part
If 2s complement is used, we can represent values like:
011010.112s = 26.7510
111110.112s = -000001.012 = -1.2510

## Slide 48: 11.2 Real Numbers Floating Point Representation
Fixed-point representation has limited range.
Alternative: Floating point numbers allow us to represent very large or very small numbers.
Examples:
0.23 × 1023 (very large positive number)
0.5 × 10-37 (very small positive number)
-0.2397 × 10-18 (very small negative number)

## Slide 49: 11.2 Real Numbers Floating Point Representation
3 components: sign, exponent and mantissa (fraction)
sign
mantissa
exponent
The base (radix) is assumed to be 2.
Two formats:
  Single-precision (32 bits): 1-bit sign, 8-bit exponent with bias 127 (excess-127), 23-bit mantissa
  Double-precision (64 bits): 1-bit sign, 11-bit exponent with bias 1023 (excess-1023), and 52-bit mantissa
We will focus on the single-precision format

## Slide 50: 11.2 Real Numbers Floating Point Representation
3 components: sign, exponent and mantissa (fraction)
sign
mantissa
exponent
Sign bit: 0 for positive, 1 for negative.
Mantissa is normalised with an implicit leading bit 1
  110.12  normalised  1.1012 × 22  only 101 is stored in the mantissa field
  0.001011012  normalised  1.011012 × 2–3  only 01101 is stored in the mantissa field

## Slide 51: 11.2 Real Numbers Floating Point Representation
Example: How is –6.510 represented in IEEE 754 single-precision floating-point format?
-6.510 = -110.12 = -1.1012 × 22
sign
exponent
(excess-127)
mantissa
1
Exponent = 2 + 127 = 129 = 100000012
10000001
10100000000000000000000
We may write the 32-bit representation in hexadecimal:
1 10000001 101000000000000000000002 = C0D0000016
(Slide 4)
11000000110100000000000000000000
As an ‘int’, it is -1060110336
As an ‘float’, it is -6.5