## Slide 1: IT5002
Tutorial #2
MIPS ProgrammIng
(Prepared by: Aaron Tan)

## Slide 2
Q1.
Palindrome
char str[size] = { ... }; // some string
int lo, hi, matched; // matched = 1 (palindrome);
// matched = 0 (not palindrome)
// Translate to MIPS from this point onwards
lo = 0;
hi = size-1;
matched = 1; // assume this is a palindrome
while ((lo < hi) && matched) {
if (str[lo] != str[hi])
matched = 0; // found a mismatch
else {
lo++;
hi--;
}
}
Variable mappings:
lo  $s0;
hi  $s1;
matched  $s3;
Base address of str[]  $s4;
size  $s5
Note:
I’ve shortened the variable names “string”, “low”, “high” to “str”, “lo”, “hi” for brevity.

## Slide 3
Q1.
char str[size] = { ... };
int lo, hi, matched;
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--;
}
}
Variable mappings:
lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4;
size  $s5
# lo = 0
# hi = size-1
# matched = 1
loop: # (lo < hi)?
addi $s0, $zero, 0
addi $s1, $s5, -1
addi $s3, $zero, 1
slt $t0, $s0, $s1
beq $t0, $zero, exit # exit if (lo >= hi)
exit:
beq $s3, $zero, exit # exit if (match == 0)
add $t1, $s4, $s0 # addr of str[lo]
lb $t2, 0($t1) # $t2 = str[lo]
Why do we use lb instead of lw?
Use slt, beq to implement blt.
(blt is a pseudo-instruction; do not use pseudo-instructions)
beq $t2, $t4, else # compare str[lo], str[hi]
add $t3, $s4, $s1 # addr of str[hi]
lb $t4, 0($t3) # $t4 = str[hi]
Study how we load data from memory: (1) prepare address in a register, (2) load using that address (with offset if necessary.)
addi $s3, $zero, 0 # matched = 0
J endW # can also be “j loop”
endW: j loop
else: addi $s0, $s0, 1 # lo++
addi $s1, $s1, -1 # hi--
else:

## Slide 4
Q1.
addi $s0, $zero, 0 # lo = 0
addi $s1, $s5, -1 # hi = size-1
addi $s3, $zero, 1 # matched = 1
loop: slt $t0, $s0, $s1 # (lo < hi)?
beq $t0, $zero, exit # exit if (lo >= hi)
beq $s3, $zero, exit # exit if (match == 0)
add $t1, $s4, $s0 # addr of str[lo]
lb $t2, 0($t1) # $t2 = str[lo]
add $t3, $s4, $s1 # addr of str[hi]
lb $t4, 0($t3) # $t4 = str[hi]
beq $t2, $t4, else # compare str[lo], str[hi]
addi $s3, $zero, 0 # matched = 0
J endW # can also be “j loop”
else: addi $s0, $s0, 1 # lo++
addi $s1, $s1, -1 # hi--
endW: j loop
exit:
add $t1, $s4, $s0 # addr. Of str[lo]
add $t3, $s4, $s1 # addr. Of str[hi]
slt $t0, $t1, $t3 # compare lo and hi addr
addi $t1, $t1, 1 # lo addr increment
addi $t3, $t3, -1 # hi addr decrement
Using “array pointer”.

## Slide 5
Q2.
(a) Set bits 2, 8, 9, 14 and 16 of b to 1. Leave the other bits unchanged.
Example: Before
b = 00110000011100000110110100100001.
(Bits 2, 8, 9, 14 and 16 are underlined.)
After
b = 00110000011100010110111100100101.
lui $t0, 1 # set bit 16
ori $t0, $t0, 0b0100001100000100 # set bits 14,9,8,2.
or $s1, $s1, $t0
Recall:
  x OR 0 = x
  x OR 1 = 1

## Slide 6
Q2.
(b) Copy over bits 1, 3 and 7 of b into a, without changing any other bits of a.
Example: Before (assume that the most significant 24 bits are all zeroes)
a = 0 0 … 0 0 0 0 1 0 1 0 1 0.
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
After
a = 0 0 … 0 0 1 0 1 0 1 0 0 0.
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
andi $t0, $s1, 0b0000000010001010
lui $t1, 0b1111111111111111
ori $t1, $t1, 0b1111111101110101
and $s0, $s0, $t1
or $s0, $s0, $t0
Recall:
  x AND 0 = 0
  x AND 1 = x
Recall:
  x OR 0 = x
  x OR 1 = 1

## Slide 7
Q2.
(c) Make bits 2, 4 and 8 of c the inverse of bits 1, 3 and 7 of b.
Example: Before (assume that the … part are all zeroes)
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
c = 0 0 … 0 1 0 0 1 0 1 0 1 0.
After
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
c = 0 0 … 0 0 0 0 1 0 1 1 1 0.
Recall:
  x XOR 0 = x
  x XOR 1 = x'
xori $t0, $s1, 0b10001010
andi $t0, $t0, 0b10001010
sll $t0, $t0, 1
lui $t1, $t1, 0b1111111111111111
ori $t1, $t1 0b1111111011101011
and $s2, $s2, $t1
or $s2, $s2, $t0

## Slide 8
Q3.
(a) c = a + b

## Slide 9
Q3.
(b) d = a + b - c

## Slide 10
Q3.
(c) c = 2b + (a – 2)

## Slide 11
Q3.
(d) d = 6a + 3(b – 2c)

## Slide 12
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
Need to trace the MIPS code with an example to find out what it does.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:

## Slide 13
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:
$s0 =
0 0 … 0 0 0 1 1 1 1 1
MSB
$t0 =
0 0 … 0 0 0 1 1 1 1 1
$t1 =
1000 0000 0000 0000 0000 0000 0000 0000
$t2 =
0 0 … 0 0 0 0 0 0 0 1
What does andi do?
Extracts the LSB of $t0 into $t2
What does xor do?
It toggles the MSB of $s0 (why?)
1
0 0 … 0 0 0 0 1 1 1 1
Example: $s0 = 31
Q: At most how many iterations?
31
Q: What happens in each iteration?
Toggle the MSB of $s0 if $t2 = 1.
Q: What is the final value of $s0 (in hexadecimal)?

## Slide 14
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:
$s0 =
0 0001010101010101010101010101010
MSB
$t0 =
$t1 =
1000 0000 0000 0000 0000 0000 0000 0000
Example:
$s0 = 0x0AAAAAAA
0 0001010101010101010101010101010
Q: What is the final value of $s0 (in hexadecimal)?

## Slide 15
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:
$s0 = 31
$s0 = 0 0000000000000000000000000011111
MSB
After:
$s0 = 1 0000000000000000000000000011111
Before:
$s0 = 0x0AAAAAAA
$s0 = 0 0001010101010101010101010101010
Before:
After:
$s0 = 0 0001010101010101010101010101010
Summary
Odd number of 1’s in $s0: MSB  1
Even number of 1’s in $s0: MSB  0.
This is known as odd parity bit scheme.
(Even parity bit scheme defined similarly.)

## Slide 16
END OF FILE