## Slide 1: IT5002
Tutorial #1
C and Number Systems
(Prepared by: Aaron Tan for CS2100)

## Slide 2
Q1.
You will learn this in week 5.
What is sign extension?

## Slide 3
Q1.
Sign extension – extending the sign bit to fill in the bit representation.
Example: from 4 bits to 8 bits.
(5)10
(0101)2s
(00000101)2s
=
=
(-3)10
(1101)2s
(11111101)2s
=
=
Note: Sign extension works for complement systems (1’s complement and 2’s complement.)
Does it work for sign-and-magnitude system?

## Slide 4
Q1.
Positive values – straightforward: (5)10 = (0101)2s = (00000101)2s
(-3)10 = (1101)2s = (11111101)2s
Negative values? Why does padding 1s in front work?
Value: –23 = –8
Value: – 27 + 26 + 25 + 24 + 23
= –128+64+32+16+8 = –8
Recall that sum of a GP = .
Here, and .

## Slide 5
Q2.
Performing subtraction in 1’s complement.
Strategy: Convert to .
Why not perform subtraction directly?
(a) 0101.11 – 010.0101

## Slide 6
Q2.
Performing subtraction in 1’s complement.
Strategy: Convert to .
(b) 010111.101 – 0111010.11

## Slide 7
Q3.
Convert the following decimal numbers to fixed-point binary in 2’s complement, with 4 bits for the integer portion and 3 bits for the fraction portion.
(a) 1.75
0.75
= 0.5 + 0.25
=
(0.1)2 + (0.01)2
= (0.11)2
Therefore 1.75 = (0001.110)2
= (0001.110)2s
or
0.752 = 1.5
0.5 2 = 1.0
end

## Slide 8
Q3.
Convert the following decimal numbers to fixed-point binary in 2’s complement, with 4 bits for the integer portion and 3 bits for the fraction portion.
(b) -2.5
2.5
= (0010.100)2
= (1101.100)2s
-2.5
= –(0010.100)2
Invert bits in 0010.100 and add 0.001
1101.011
+ 1
1101.100

## Slide 9
Q3.
Convert the following decimal numbers to fixed-point binary in 2’s complement, with 4 bits for the integer portion and 3 bits for the fraction portion.
(c) 3.876
0.8762 = 1.752
0.7522 = 1.504
0.5042 = 1.008
0.0082 = 0.016
0.876
= (0.1110)2
(0.111)2
Therefore 3.876 = (0011.111)2
= (0011.111)2s

## Slide 10
Q3.
Convert the following decimal numbers to fixed-point binary in 2’s complement, with 4 bits for the integer portion and 3 bits for the fraction portion.
(d) 2.1
0.12 = 0.2
0.22 = 0.4
0.42 = 0.8
0.82 = 1.6
0.1
= (0.0001)2
(0.001)2
Therefore 2.1 = (0010.001)2
= (0010.001)2s

## Slide 11
Q3.
Using the binary representations you have just derived, convert them back into decimal.
(d) 2.1
(a) 1.75
(b) -2.5
(c) 3.876
= (0001.110)2s
= (0001.110)2
= (1101.100)2s
= –(0010.100)2
= (0011.111)2s
= (0011.111)2
= (0010.001)2s
= (0010.001)2
(0001.110)2
= 20 + 2-1 + 2-2
= 1.75
–(0010.100)2
= –(21 + 2-1)
= –2.5
(0011.111)2
= 21 + 20
+ 2-1 + 2-2 + 2-3
= 3.875
(0010.001)2
= 21 + 2-3
= 2.125

## Slide 12
Q4.
How would you represent the decimal value -0.078125 in the IEEE 754 single-precision representation? Express your answer in hexadecimal.
-0.078125
= -(0.000101)2
= -( 1.01 )2  2-4
1
Sign-bit
8-bit exponent
23-bit mantissa
01000000000000000000000
Exponent: -4 + 127
= 123
= (01111011)2
01111011
1 01111011 01000000000000000000000
B
D
A
0
0
0
0
0

## Slide 13
Q6.
Trace the program manually and write out its output.
int a = 3, *b, c, *d, e, *f;
b = &a;
*b = 5;
c = *b * 3;
d = b;
e = *b + c;
*d = c + e;
f = &e;
a = *f + *b;
*f = *d - *b;
printf("a = %d, c = %d, e = %d\n", a, c, e);
printf("*b = %d, *d = %d, *f = %d\n", *b, *d, *f);
a
c
e
b
d
f
3
5
15
0
This does NOT make d point to b!
This copies the content of b into d.
20
35
55
Output:
a = 55, c = 15, e = 0
*b = 55, *d = 55, *f = 0

## Slide 14
END OF FILE

## Slide 15
Given a number x which can be expressed as an n-bit binary number, its negated value can be obtained in 2s-complement representation using: -x = 2n – x
Example: x=12; Assume 8 bits, -x = 28 – 12 = 244 = (11110100)2s
Technique: invert the bits then plus 1. 12 = (00001100)2s  -12 = (11110100)2s
2s complement
Given a number x which can be expressed as an n-bit binary number, its negated value can be obtained in 2s-complement representation using: -x = 2n – x – 1
Example: x=12; Assume 8 bits, -x = 28 – 12 – 1 = 243 = (11110011)1s
Technique: invert the bits. 12 = (00001100)1s  -12 = (11110011)1s
1s complement
For reference.

## Slide 16
10.4 Comparisons
4-bit system
Positive values Negative values
Important!
Value | Sign-and-Magnitude | 1s Comp. | 2s Comp.
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
+0 | 0000 | 0000 | 0000
Value | Sign-and-Magnitude | 1s Comp. | 2s Comp.
-0 | 1000 | 1111 | -
-1 | 1001 | 1110 | 1111
-2 | 1010 | 1101 | 1110
-3 | 1011 | 1100 | 1101
-4 | 1100 | 1011 | 1100
-5 | 1101 | 1010 | 1011
-6 | 1110 | 1001 | 1010
-7 | 1111 | 1000 | 1001
-8 | - | - | 1000
For reference.